## Slide 1: Internet Technologies
CSC457

## Slide 2: Network and Internetwork
When two or more devices have to be connected for data sharing or resources or exchanging messages, we call it networking.
There is a difference between networking and internetworking.
  In networking (LAN) all the devices are compatible with each other.
  It may or may not be the case in internetworking.
    Differences in hardware and software make systems incompatible.

## Slide 3: The Underlying Technologies
Underlying technologies that make internet work so successfully are:
  Packet Switching
  Routers
  TCP/IP
  Clients + Servers = Distributed Computing
  Computer Names.

## Slide 4: Packet Switching
Because of various limitations communication is broken up into packets.
Each packet starts at the source and is communicated hop by hop across the routers to the destination.
Each packet is labeled.
  Each packet has a serial number used for reassembly of the message.

## Slide 5: Packet Switching
Packet’s header contains source & destination addresses.
  Destination address is used for forwarding (routing)
Packet’s header also contains CRC (cyclic redundancy check)
  Used for error control.
Packets are not all the same size.

## Slide 6: Packet Switching
Two ways of path selection:
  Virtual circuit
    More like circuit switching. Path is preselected and will stay the same for entire communication.
  Datagram
    Path is not predetermined. Packet is sent to the next node on the route which is best at that time.
    Each packet may follow different path.
Can be retransmitted if packet get corrupted (using CRC) or lost.
  ACK, NACK and timeout helps in detecting problems with the packet.

## Slide 7: Packet Switching
In case of error only one packet will need to be retransmitted.
Efficient use of resources by sharing.
Fine for text, web pages.
A typical text email message takes up a few packets.
Audio takes a stream of thousands of packets.

## Slide 8: Router
A router interconnects two or more compatible or incompatible networks (Ethernet, IBM Token Ring, FDDI, ATM.).
Its a small computer with network interfaces, memory and program dedicated to packet switching function.
Translates data between the networks if there is a need.
Each router moves an entire packet from one connection to another.
Packets for each connection is held in a queue.

## Slide 9: Routers
Selects the best route possible between the interconnected networks.
Data delivery from one computer to another is accomplished through store-and-forward technology.
Stores incoming packet and forwards the packet to another switch or computer.
  In case outgoing connection is busy or down.

## Slide 10: TCP/IP
TCP/IP stands for Transmission Control Protocol/Internet Protocol.
TCP/IP is the communication protocol for the Internet.
The Internet communication protocol defines the rules for computer communication over the Internet.
Browser uses TCP/IP to access Internet servers, and servers use TCP/IP to send HTML back to your browser.

## Slide 11: TCP/IP
Inside the TCP/IP standard there are a number of protocols for handling data communication:
TCP (Transmission Control Protocol) communication between applications.
UDP (User Datagram Protocol) simple communication between applications.
IP (Internet Protocol) communication between computers.
DHCP (Dynamic Host Configuration Protocol) for dynamic addressing.

## Slide 12: TCP/IP
TCP/IP is TCP and IP working together.
TCP takes care of the communication between your application software (i.e. your browser) and your network software.
IP takes care of the communication with other computers.
TCP is responsible for breaking data down into IP packets before they are sent, and for assembling the packets when they arrive.
IP is responsible for sending the packets to the receiver.

## Slide 13: TCP/IP
TCP/IP is a large collection of different communication protocols based upon the two original protocols TCP and IP.
  HTTP - Hyper Text Transfer Protocol for communication between a web server and a web browser.
  HTTPS - Secure HTTP for secure communication between a web server and a web browser.
  SMTP - Simple Mail Transfer Protocol is used for transmission of e-mails.

## Slide 14: TCP/IP
TCP/IP is a large collection of different communication protocols based upon the two original protocols TCP and IP.
  MIME - Multi-purpose Internet Mail Extensions lets SMTP transmit multimedia files including voice, audio, and binary data across TCP/IP networks.
  POP - Post Office Protocol is used for downloading e-mails from an e-mail server to a personal computer.
  FTP - File Transfer Protocol it takes care of transmission of files between computers.

## Slide 15: Applications
Some applications of the Internet:
  World Wide Web (WWW)
  Electronic Mail (Email)
  Bulletin Boards (Newsgroups)
  Audio & Video Services

## Slide 16
Internet Topology
Backbone Network
Network Access Provider (NAP)
Internet Service Provider (ISP)
Users
Users
Users

## Slide 17
Internet Topology (Detailed)
Backbone Network
Users
R
R
R
R
NAPn
R
NAP1
R
NAP2
R
NAP3
R
ISP
R
ISP
R
ISP
R
ISP
R
R
R
R
R
Users
Users
Users
Users
R
= router

## Slide 18: Internet Toplology
At the top level there is backbone
At the intermediate level there are:
  Network Access Providers (NAP).
  Internet Service Providers (ISP).
A user connects to an ISP to connect to the internet.
An ISP routes the call to a NAP.
It may cross the backbone network to reach the final destination.

## Slide 19
A Typical ISP
Subscriber1
Subscriber2
Subscriber3
Subscribern
modem1
modem2
modem3
modemn
Internet
Server
ISP Setup

## Slide 20: Ways of Connecting your Computer to the Internet
The Internet
So what is "the Internet"? The Internet is a gigantic collection of millions of computers, all linked together on a computer network. The network allows all of the computers to communicate with one another. A home computer may be linked to the Internet using a phone-line modem, DSL or cable modem that talks to an Internet service provider (ISP). A computer in a business or university will usually have a network interface card (NIC) that directly connects it to a local area network (LAN) inside the business. The business can then connect its LAN to an ISP using a high-speed phone line like a T1 line.

## Slide 21: Ways of Connecting your Computer to the Internet
ISPs then connect to larger ISPs, and the largest ISPs maintain fiber-optic "backbones" for an entire nation or region. Backbones around the world are connected through fiber-optic lines, undersea cables or satellite links
In this way, every computer on the Internet is connected to every other computer on the Internet.

## Slide 22: Ways of Connecting your Computer to the Internet

## Slide 23: Ways of Connecting your Computer to the Internet
LAN – (Local Area Network)
  Available at work or university
  Usually highest speeds.
  Connected to Internet through a router or a bridge.
ADSL – (Asymmetric Digital Subscriber Line)
  Allows for very high-sped connections over existing telephone wires.
  ISP must provide ASDL service

## Slide 24: Addressing on the Internet
A physical address (or MAC address) is permanently embedded in a network interface card and identifies a device on a LAN.
An IP address identifies a computer, printer or other shareable device on the Internet
A domain name is an easy-to-remember word for an IP address. It is an alias.
A port address is a number that identifies a program running on a computer.

## Slide 25: Addressing on the Internet
Physical addresses or MAC (Media Access Control) addresses – are unique identifications put on every network card on every computer on a network. They allow computers on the same network to communicate.

## Slide 26: Addressing on the Internet
An IP address identifies a computer, printer or other device on the Internet.
  Dynamically assigned IP addresses - are what is used when you log on to the Internet via an ISP. You are temporarily assigned an address when you use their service to get on the Internet.
A domain name is an easy-to-remember word for an IP address.

## Slide 27: Addressing on the Internet
A single computer can be running several applications (email, FTP, HTTP and others).
A port is a 16-bit number allocated to a particular software (application) or services running on a computer.
TCP is application to application (port to port).
TCP uses port numbers to identify different application running on a single computer.
A socket = IP address with port number. e.g. 169.49.209.19:20

## Slide 28: Ports and Socket A Typical Scenario
When a client application sends a TCP request to a server application, it provides server application port number.
The TCP software on client allocates an unused port number to that client application.
The server receives the request and TCP software passes it to the intended server application.
The server replies with its own port number and the client port number.

## Slide 29: Ports and Socket A Typical Scenario
Client
From Source port number = 80
Destination port number = 23
Source port number = 23
Destination port number = 80
Source

## Slide 30: What is web?
Web is the collection of documents, text, voice or video, stored on Internet.